Central Pennsylvania Repeater Association Inc.

W3ND February 2009

NOTICE: the next general meeting will be at 7:30 PM Thursday, February 19th, 2009 at Tyco, 100 Amp Drive, Harrisburg.

A message from our president: From WA3CPO, Gary Blacksmith, MD

Repeater upgrade progress:

145.47 excellent coverage,

The ARCOM RC-810 controller will be removed & bench tested

444.45 functions well, coax 1-5/8”, coverage to East reduced due to tower shading of pattern.  Future antenna change to upper West UHF Collinear.

10.369 Beacon driver failure, sent back to factory.

145.29  IRLP operational, coverage excellent internet installed, 1500/1500                        Software ID failure

3480 ATV 7/8” coax installed , 10 GHz link needs video adj. NASA dish needs relocated, camera not installed.  Xmtr in Beacon mode as needed.

6 meter  antennas need installed on roof: rec & uhf xmtr.

144.97 Packet taken out of service.

APRS   Will stay at Reeser’s Summit.

N3TWT APRS to be tested on VHF upper West ant.

146.94 Repeater off line, looking for a new home ?

Antenna Progress

Six antennas on WITF Standby Tower

- 4-Bay VHF high on East side, Operational

7/8” Commscope continuous run (145.29)

- 4-Bay VHF Mid on East side, Operational

New ½” Andrew with 50’ extension (145.47)

- Collinear UHF Mid on West side, Operational

1-5/8” Andrew continuous (444.45)

4.  	ATV 3.4 GHz collinear, Operational

7/8” Andrew, spliced

- 4-Bay VHF high on West side

Needs splice 7/8” to 1-5/8” (future APRS)

- Collinear UHF high on West side

Needs splice 7/8” to 1-5/8” (future 444.45)

K & C has started to complete coax installation of VHF & UHF antennas High on West side.

Terry Phillips, KA3AAA, will be removing an unused coax from under the ice bridge and inspect the rubber roof as needed

Paul Coleman, KB3NFZ will be adding strut on the west side of the Building for a satellite antenna

Rooftop Antennas

- 10 GHz Beacon, sent out for repair

- 10.4 GHz receive dish from White Rock, Operational

- NASA receive dish from Dish Network TB relocated

- UHF omni for control receiver, Operational

Generator Status- None

Dauphin County has been approached about a 5 KW propane generator that will be taken out of service.  Our demand is less than 1000 watts.  A separate room is available for this purpose.

MISC. INFORMATION

145.11 & 448.075 repeaters at Ellendale, Operational

147.075 PEMA/EOC repeater now operational at Ellendale with a PL of 123.

Has anyone seen the six meter Ringo antenna that was behind our new Shelter?  We would like to use it on the roof of the shelter for the six meter receive antenna.

PEMA has agreed to host the wireless internet antenna. That will give us access to this donated source for the internet.  We tried to receive it from the top of our new shelter but could not.  Obstructions prevented us from receiving the signal from TV-27s tower. PEMA now has an alternate access to the internet.

They also gave permission to install a 5.8 GHz Ethernet bridge from PEMA to our shelter on Blue Mountain.

This 48 Mbps connection will allow the internet to be relayed up to the mountain.  It would also serve as a data connection from PEMA to an expanded eight county network.  The internet is installed and is functioning at the PEMA RACES room.  1000/1000 is also being sent up to Blue Mountain to test the link.

The old Motorola Micor UHF repeater will be relocated after testing and refurbishment to Lam’s Gap. The SMRA UHF repeater failed and replacing it was not justified based on the usage.  An antenna, coax, and duplexer are still on site.  The Lam’s Gap UHF repeater will be tied full time once equipment is available to the 444.45 MHz repeater at Blue Mountain.  That would give portable coverage on the East shore and West Shore.  The plan is to add a third UHF repeater at Reeser’s Summit and tie that full time into the other two repeaters.  That would add portable coverage to South Harrisburg, TMI, and MDT.  The Eight County exercise Wide Vigilance II demonstrated the lack of portable coverage at TMI and MDT.

The recent high winds caused damage to the support for the West side upper antennas.  The mount rotated in toward the tower. The ankle iron has cracked during tightening  and now the entire mount needs replaced. The above photo is not a current view.  The support to the 4-bay antenna in the lower right of the picture is just fine.

The meeting this month will be held on Thursday, February 19 from 7:30 PM to 9:00 PM at M/A-Com (Tyco) 100 Amp drive, Harrisburg.  We will discuss the growth of the high speed data link from CPRA, Inc.  Likely links include: Cornwall, Dauphin Co RACES room, Reeser’s Summit, Cumberland Co RACES room.

Cornwall could then build a link to the Lebanon Co RACES room and to Lancaster Co Emergency Management and the Task Force HQ (MACC) at the Lancaster Training Facility.  The link at Reeser’s Summit can be connected to the W3HZU club house.  From W3HZU the York Co RACES room and the Adams Co RACES room can be added to the network. Outside funding has not been requested yet.  The links are rather inexpensive and could be funded by amateurs in each county.

The initial link from PEMA to the CPRA location on Blue Mountain is installed and works well. The link from Blue Mountain to Reeser’s Summit has been tested on the bench.  The throughput from PEMA to Reeser’s Summit is excellent.  We put 1000/1000 in at PEMA and were able to get 1000/1000 out of the Reeser’s Summit equipment.  Chris Bunting is building a server to be placed at PEMA that contains a mail server, web server, and a FTP server. Financial support is needed to add a sector antenna ($150) and a one watt transmitter ($100) at Blue Mountain to provide wide area coverage to Dauphin County.  This would include the Dauphin Co EOC, all the hospitals, and interested amateurs. Other possible uses of the network include transporting audio between repeaters and transporting video between ATV repeaters with NTSC to IP converters.

This week SMRA will have a presentation about the benefits of building a data link in Cumberland County.

ARES AND RACES:  From Your Editor, Roger, W3HUP

PEMA NETS AND FREQUENCIES:

Central Area meets on   3993.5 kHz every Sunday at 8:30 AM Local

Eastern Area meets on  3987.5 kHz every Sunday morning at 9:00 AM Local

Western Area meets on 3990.5 every Sunday morning at 9:00 AM Local

Our PA State Net meets the FIRST SUNDAY of every month on 3993.5 kHz at

8:00 AM Local.  This net is usually called by John Kruk, K3KR, Lock Haven; at which time he calls Eastern, Central and Western Area Stations in that order.

The New York State net usually meets on 3993.5 kHz at 9:00 AM right after our Central Area net.....

Central Area PEMA frequencies are:

3993.5 kHz  -  Primary

3984.5 kHz  -  Alternate

3999.5 kHz  -  Alternate

7248.5 kHz  -  Alternate

7250.5 kHz  -  Alternate

ON-LINE Operator Training Course Availability:

You need the content of both FEMA and ARRL training courses.  Follow the link below to get to the FEMA training web site for all the FEMA stuff you might be interested in…PEMA also offers many of the same courses.  The Emergency Management Institute (EMI) offers a broad range of NIMS related training.

www.training.fema.gov/EMIWeb/IS/crslist.asp

Minimum training requirements are the ICS 100 and 700 certifications which can be completed in a day or two each on-line at your own pace. They are needed for both ARES and RACES operators; we are all one pool of operators.

These classes cover what you will need in emergency situations to work with any agency.  They cover the National Incident Management System (how emergency management is organized and how volunteers such as us fit in to the process).  You will also need the Amateur Radio Emergency Communications Course Level 1 (preferably Level 2 as well), available from the ARRL, which cover Amateur Radio emergency operating procedures.  And…listen to how the nets operate!  While you don’t have to get all this stuff at once, you should be working on it now so you will have it by April in time for the TMI Drill.

PINNACLE HEALTH SYSTEM ID CARDS: Your Editor, Roger, W3HUP

Repeat announcement: Here is your opportunity to help out with emergency  communications during the time of need. All the hospitals now have amateur radio equipment installed in them.  Most hospitals will need operators as well.

If you want to help out at Pinnacle Health System, you will need one of their ID cards to access their ham radio equipment. If you are interested please contact Ms. Patte Shambaugh at 717-782-3347 to make an appointment for your ID Card.

Photos can be taken daily from 7:30 until 4:00. Pinnacle Health will require you to fill out some paperwork for the hospital system.  If you get an ID card for Pinnacle, please let your VP know, Terry Phillips, KA3AAA so he can put you down as an operator for the hospitals in the Harrisburg area.  But don’t forget the need for ARES and RACES operator training as discussed above

ATV Report:  From WA3CPO, Gary Blacksmith, MD

No additional activity over the past month.  Once the weather improves we will be able to make improvements to the White Rock and Blue Mountain sites.  W3HZU will also be climbing their tower to install a 3480 MHz transmit antenna.

The new data network may transport video between ATV sites in addition to conventional analog FM 10 GHz microwave.

The Lancaster area may be making improvements at SPARC.  Funding was requested for ATV at Cornwall. That would provide a signal to the Lancaster EOC and the MACC.  Does anyone have analog video to IP servers available?

TREASURER’S REPORT: By Dave Hoffman, N3PRO

We are currently running $500.00, our electric bill is averaging $75.00 per month, we receive $12.50 per month from HRAC for the 146.76 which was figured on one third the electric bill for three month.  Since that time we have added IRLP 145.29, ATV, and the 10 GHZ beacon.  The renewal applications will be mailed out with the ballots as soon as they are finalized.  I had planned to have them out by now, but we are in need of a secretary and two alternates; I had a plea sent out a few weeks ago and no responses.  Anyone interested please contact me ASAP, N3PRO@comcast.net.

Miscellaneous:

Anyone remember the days of J.R.S distributors in York?  Pictures are on the Keystone VHF site at www.w3hzu.com, click on gallery on the left side then JRS distributors under the title History.  

As I am in Winchester Virginia right now, had a few opportunities to try out our node from here using the 145.21, thanks Kevin KA0JQO for getting this up and running.  Very little activity down hear except the 147.300, 147.255, and APRS so it was nice to talk back home if it it’s not all that far.  

Try out the new PEMA repeater on 147.075 PL 123.0.  It went on the air just as I was leaving.  I lost it about Shippensburg, around mile marker 27 on 81.  It is at Ellendale Forge where the 145.11 is  NOT Blue Mountain or Peters Mountain as it is wrongly talked about.

“BOILER PLATE”: From your editor, W3HUP

Officers, Board, and Committee Members

President:			WA3CPO Gary Blacksmith, MD
V. President:		KA3AAA Terry Phillips
Secretary:			N3NZI Marty Ginter

Treasurer:			N3PRO Dave Hoffman
Past President:		K3SZX Alan Abt
Trustee for W3ND:		KA3AAA Terry Phillips

Member at large:		WA3MMD Bob Kurtinecz

Member at large:		N3JQM Neil Shatto
Member at large:		AA3T Nick Rylatt

Alternates:			KA0JQO Kevin Maglouglin

Web Master:			WB3DRT Lee Schwan

IRLP Committee:		WA3HDP Ken Sutton

WB3CKW Gerard Whisler

WA3MMD Bob Kurtinecz

RACES team:		WB3BKN Terry Snyder, RACES R/O

K3JJK Lee Ash, and N3JQM Neil Shatto

Public Relations:		W3KB Keith Beebe

Recruitment	:		KZ3J Curtis Zell

News Letter Editor:	W3HUP Roger Urban

Facilities with the CPRA club call sign W3ND:

144.39	APRS node from Reeser’s Summit.

144.97  	NetRom Node Digipeater

145.11-	Dauphin County RACES repeater, CTCSS 123.0 Hz

  - IRLP node 7060 Blue Mtn. IRLP  CTCSS 88.5Hz

  - Med coverage, Blue Mtn, auto patch ** ##, CTCSS 123.0Hz

146.94-	In-town/in-building coverage.

444.45+  	Medium coverage from Blue Mountain

448.075-	Dauphin County RACES repeater. CTCSS 123.0 Hz

53.01-           On the air with some RX sensitivity problems.

Monthly Ham Radio Lunch: at the Old Country Buffet in east Harrisburg the last Thursday of each month at noon unless it is a major holiday.  This restaurant is located on route 22 in Colonial Park in the vicinity of Value City Furniture, K-Mart and Home Depot.  Good way to meet some new people!

Club Web Site:   http://cpra.home.att.net

Pay it a visit…we have links to various services, general information and the current and back issues of the Newsletter.  Also, note there are some changes on the Board of Directors this year!

Dues: are $20/yr for a single membership and $35/yr for a family membership, which includes all licensed amateurs living in one household.

use the revised membership application BELOW.

Thanks!   Please make your check payable to:

Central Pennsylvania Repeater Association, Inc.

2130 Cedar Lane,  Enola, PA  17025-3319

DO NOT SEND CASH!

APPLICATION FOR MEMBERSHIP IN CPRA

□ New member    □ Renewal   □ Family   □ Updating Information              □ Donation ______________     □ Other ______________________

Total amount enclosed $ ____________

Prorated April to April payment schedule, please follow below.

April – October        $ 20.00    Family $ 35.00

November – March $ 10.00    Family $ 15.00

Name:___________________________________   Call(s)_________________

Address: ______________________________  City: ______________________

State: ________  Zip code __________  License class:  ___________________

Email address for newsletters: ________________________________________

Phone: _______________________  	   □ Listed               □ Unlisted

Are you an ARRL member?   □ Yes         □ No

Are you a member of WITF    □ Yes         □ No

EMERENCY RACES VOLUNTEER INFORMATION

This information will only be used in the event of an emergency.  This information will only be given to the emergency RACES coordinator and will not be distributed for general information in any form!

Work number including extension:  _______________________________

Cell Phone:  _________________________________________________

Email address:  ______________________________________________